## Slide 1
1GSK Consumer Healthcare, Weybridge, Surrey, UK; 2University of Witten/Herdecke, Witten, Germany
The In Vitro Efficacy of Various Toothbrush Parameters
Alyson A,1 Mueller WD,1 Rafferty H,1 Lang T,2 Gängler P2
Eight Dr. BEST® (GSK Consumer Healthcare, Brentford, UK) toothbrushes were tested using a clinically validated, comparative robot test5 to examine in-vitro brush efficacy
  KaVo™ typodonts were used: four incisors, one canine, two premolars, three molars in anatomic positions, coated in simulated plaque
  Five runs each of five horizontal, five rotating and five vertical movements at 3.5 N
Evaluation of plaque removal carried out using automated plaque planimetry
  30 planimetrical fields per tooth encompassing 13 areas representing buccal, lingual and proximal sites of tooth crowns and exposed tooth roots
  For each comparison (below), Kolmogorov-Smirnov-test applied to analyse the 13 areas, nine analysed by independent two samples t-test combined with Leven test, null hypothesis of normality rejected for four areas so analysed by non-parametric Wilcoxon-Mann-Whitney U-test
Poster No. 3074
Toothbrushing reduces plaque levels and, hopefully, the risk of plaque-associated diseases such as dental caries, gingivitis and periodontitis1,2
Manual toothbrushes have a number of parameters that can impact efficacy
  Most guidelines recommend a small head with bristles that are medium or soft, tapered and provide interdental cleaning3,4
This in vitro study examined the most frequently adjusted design parameters during manual toothbrush development and compared them with regard to plaque-removal efficacy
In some comparisons, one head style clearly removed significantly more plaque
  Smaller filament diameter/lower hardness:
    S3 (0.12 mm diameter) overall removed significantly more plaque than S4 (0.15 mm diameter), predominately with horizontal and rotating brushing movements
    S4 (0.15 mm diameter, soft) overall removed significantly more plaque than S2 (0.23 mm diameter, medium hard), predominantly with horizontal and rotating brushing movements
  Higher cutting height: S2 (tuft height 12 mm) overall removed significantly more plaque than S5 (tuft height 9 mm) with all brushing movements
In other comparisons, overall superiority was less clear cut
  ? Smaller head size: S1 (compact head) removed significantly more plaque overall using horizontal and rotating brushing movements than S2 (full head) but the latter was superior overall using vertical brushing movements
  ? Less interdent height difference: S8 (tuft heights 8.5/11 mm) removed significantly more plaque than S7 (tuft heights 10/11 mm) with rotating and vertical brushing movements but S7 was significantly superior with horizontal brushing movement
  ? Lower hardness/filament diameter:
    While overall S6 (0.18 mm filament diameter, soft) removed significantly more plaque than S2 (0.23 mm, medium) (H/R movements), in some areas S2 was superior
    S4 had thinner filaments than S6 (0.15 mm, soft) and was superior lingually and in some buccal areas, but S6 (0.18 mm, soft) was superior in mesial and distal areas and overall with rotating movements
Aims
Methods
Results
Presented at the IADR General Session, Washington DC, USA, March 18–21, 2020
Brushes that allow the bending and flexing of bristles (longer, softer) with smaller parameters (head size, filament diameter) removed significantly more simulated plaque with most brushing movements than brushes with shorter, harder bristles and larger heads
Findings of in vitro plaque removal superiority of one toothbrush head design over another can be used to improve toothbrush design to the benefit of the consumer in a real-world setting
Conclusions
References
1) Fejerskov I. Dental caries: The disease and its clinical management. Blackwell Munksgaard. 2008; 2) Löe HJ. Int Dent J 2000;50:129–39; 3) Gallob J, et al. J Clin Dent 2016;27:39–47; 4) Hoogteijling F, et al. J Dent Hygiene 2018;16:3–12;
5) Lang T et al. BMC Oral Health 2014;14:82
Acknowledgements
  This study was funded by GSK Consumer Healthcare, from whom the University of Witten/Herdecke received funding
  Editorial support was provided by Dr Eleanor Roberts of Beeline Science Communications, Ltd
Brushing movements: H: Horizontal; R: Rotating; V: Vertical
Statistically significant higher percentage plaque removal corresponds to toothbrush colour coding (Black or Orange)
ABCDF: Risk fields near the gum line and approximally between the teeth; W: Tooth root sites Total: Total mean plaque reduction over all tooth sites
*p<0.05; **p<0.01; ***p<0.0001; NS: No significant differences with any brushing movement
Head size
S1: R5 Compact head Vs S2: R5 Full head
Filament diameter
S3: R5 Full head Vs S4: R5 Full head
Filament diameter 0.12 mm Filament diameter 0.15 mm
Cutting height
S5: R5 Full head Vs S2: R5 Full head
Tuft height 9 mm Tuft height 12 mm
Hardness
S6: R5 Full head Vs
Soft, Filament diameter 0.18 mm S2
Medium
0.23 mm
S4
Soft
0.15 mm
Interdent height difference
S7: G5 Interdental cut Vs S8: G5 Interdental cut
Tuft height 10 mm and 11 mm Tuft height 8.5 mm and 11 mm
 | Head size | Filament diameter | Cutting height | Hardness |  |  | Interdent height diff
 | S1 v S2 | S3 v S4 | S5 v S2 | S2 v S4 | S2 v S6 | S4 v S6 | S7 v S8
Buccally | R*V** | R* | H**V** | H*R** | NS | H*R** | H**R*V*
W Buccally | V** | H*R** | H*R*V** | H**R** | R**V** | R* | R**V*
ABCDF Buccally | H*V*** | H** | H***R*V*** | H***R*** | V*** | H**R**V*** | H***R***V**
Lingually | R*V* | H* | H**V* | H**R** | H**R**V* | H**R** | H*R**V**
W Lingually | R* | H*** | H***V*** | R*** | R** | H*R** | H**R***V*
ABCDF Lingually | H*V*** | H*** | H***V*** | H**R*** | H*V*** | H***R**V** | H***R***V**
Mesially | H*R* | H***R*** | H**V*** | H*R** | H***R**** | H**R*** | H***R***V*
W1 Mesially | R** | H**R***V* | H***V*** | H***R*** | H***R*** | H***R*** | H*R***
W2 Mesially | H**R*** | H***R** | H***V*** | H*R*** | H***R*** | H**R** | H***R***
Distally | NS | H***R***V* | H**R*V*** | H*R*** | H***R***V*** | H***R***V** | H***R**V**
W1 Distally | NS | H***R**V*** | H***R**V*** | H*R***V*** | H***R***V*** | H***R** | H***R**V*
W2 Distally | H* | H***R***V* | H***R**V** | H***R*** | H***R***V*** | H**R**V** | H***R***V**
Total | H*R**V* | H**R* | H**R*V* | H**R* | H**R*** | R* | H*R**V**
Table 1: Statistical analysis of cleaning efficacy (% plaque removal)